## Slide 1
Supporting reduction of risks of tailings dams using earth observation data
Mark Davison, Marta Roca, Gregor Petkovsek HR Wallingford, Wallingford UK

## Slide 2
Closed tailing deposits
Abandoned tailing deposits
Release of tailings causes:
loss of life
pollution and environmental damages
economic losses
The problem …
Active tailing storage facility

## Slide 3
Their failure, as seen for example in January 2019 with the fatal failure of Brumadinho dam in Brazil, can cause:
    loss of life (270 to 330 fatalities)
    irreversible damage to ecosystems
    large economic damages

## Slide 4
A multidisciplinary project team from UK and Perú
Funded by
We developed
DAm Monitoring with SATellites
How do we address the problem?

## Slide 5
We designed a multidisciplinary approach to monitoring tailings storage facilities
This will help users to:
assess the overall status of each site
target their monitoring resources efficiently
contribute to the reduction of environmental and social impacts downstream
Site information
Pollution detection
Movement detection
Hydrological forecast
Emergency planning
Data integration & assessment
Visualisation

## Slide 6
Focus on… emergency planning
Defining the dam breach With a multi-layer model
  EMBREA-MUD
Defining the hazard With a 2D mud flow model
  MIKE-21 Mudflow
Estimating the impact downstream With an agent based evacuation model Life Safety Model (LSM)

## Slide 7
Breach modelling – EMBREA-MUD
  A two fluid dam break model
  Simulates the evolution of the breach opening
  Validated on
    Merriespruit tailings dam failure in South Africa in 1994
    Mount Polley tailings dam failure in Canada in August 2014 (see Petkovšek et al., 2020)
EMBREA-MUD
  Sunny day failure
  Failure with extreme rainfall / inflow
Scenarios
  Outflow hydrograph for mud
  Outflow hydrograph for water
Outputs

## Slide 8
Breach modelling with EMBREA-MUD

## Slide 9
  MIKE21 Mudflow
  2D model
  full Bingham model for mudflow
Mudflow model
  2D defined based on a 12.5m horizontal resolution DTM.
  Inputs to the MIKE 21 mudflow model are:
    fluid density in kg/m3,
    yield stress in N/m2
    dynamic viscosity in kg/m.s
Model setup
  Mudflow depths and velocity
Outputs
Mudflow modelling

## Slide 10
Mudflow modelling results

## Slide 11
Impact on people – Scenarios considered in the Life Safety Model (LSM)
  Night time and day time populations
  No warning issued
Baseline impact
  Warnings issued at the start of dam failure
  Warnings issued prior to dam failure
Warning scenarios
  Range of response times from 1 to 15 minutes
  Choice of evacuation routes
  Method of travel
Evacuation response scenarios
  Agent based model of the interaction of people and flood hazard. Inputs:
      Population, building locations, road network
      2D hazard results
LSM

## Slide 12
Contains Copernicus Sentinel data [2019]
Unaware
Aware
Evacuating
Safe
Injured
Deceased
Mudflow depth (m)

## Slide 13
Impact on people – a summary
  ~1,500 fatalities with 93% Fatality Rate
Significant loss of life if a warning is not given
  Fatalities to in the range 50 to 500 depending on the speed that people respond to the warning
  Not sufficient time for those close to the dam
Warning issued at the point of failure could significantly reduce fatalities
  Warning issued 1 to 2 hours before failure would allow enough time to evacuate provided people know how to respond
Adequate warning can significantly reduce loss of life
Late warning could increase fatalities if evacuation routes are in the risk zone

## Slide 14
Project team:
Funded by:
more information at www.damsat.org