## Slide 1: An operational system for tailings dam monitoring by bringing together remote sensing, meteorological and on-site observations
Marta Roca, Eleanor Ainscoe, Gregor Petkovsek, Mark Wetton, Ye Liu, Mark Davison, Alberto Riera HR Wallingford, Wallingford UK

## Slide 2
Tailings dams are earth embankments used to store toxic mine waste and effluent.

## Slide 3
Their failure, as seen for example in January 2019 with the fatal failure of Brumadinho dam in Brazil, can cause:
    loss of life
    irreversible damage to ecosystems
    large economic damages

## Slide 4
Tailings dams risk of dangerous occurrences - Lessons learnt from practical experiences, ICOLD Bulletin 121, 2001
See also: A review of the risks posed by the failure of tailings dams, Roca et al. 2019
Chart: Number and cause of tailings dam failures 1917-2000
| Overtopping | Slope instability | Earthquake | Foundation failure | Seepage and internal erosion | Structural failure | Erosion | Mine subsidence | Unknown
Active Dams | 20 | 30 | 18 | 11 | 10 | 12 | 3 | 3 | 15
Inactive Dams | 8 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 3
Tailings dams can fail via various mechanisms:

## Slide 5
For the DAMSAT project we designed a multidisciplinary approach to monitoring tailings storage facilities
This will help users to:
assess the overall status of each site
target their monitoring resources efficiently
contribute to the reduction of environmental and social impacts downstream
Site information
Pollution detection
Movement detection
Hydrological forecast
Emergency planning
Data integration & assessment
Visualisation

## Slide 6
We apply a change detection algorithm based on image differencing of Sentinel-2 MSI satellite images…
…to identify suspected spills and leakage
Because some pollution can’t be detected directly but may effect vegetation health, we also assess changes in NDVI (normalised difference vegetation index)
Contains modified Copernicus Sentinel Data 2020
December 2018
tailings spill

## Slide 7
DAMSAT uses time series analysis of satellite InSAR from the Cosmo-SkyMed and Sentinel-1 constellations…
to produce graphs and maps of dam displacement in the line-of-sight direction over recent months
Contains modified Copernicus Sentinel Data 2020
Date
At some sites in-situ GNSS instruments are installed to give higher accuracy and higher temporal resolution measurements

## Slide 8
Hydrological forecasting
We use meteorological forecasts and hydrological models…
…to forecast runoff into the tailings pond…
…and the resulting changes in water level
Rainfall
Water discharge
Increase in water level

## Slide 9
Alongside the monitoring, we use dam breach, inundation and evacuation models…
…to estimate loss of life and economic damages that could result from failure…
…to assist emergency planning and provide a better understanding of the impacts if a failure occurs
See more in Mark Davison’s presentation, Thursday 7th May 16:15-18:00 in session NH9.6
Emergency planning

## Slide 10
The DAMSAT system is being developed and tested on sites in Peru, focussing on the mining regions of Cajamarca and Cerro de Pasco
Basemap © NASA, TerraMetrics, GoogleEarth

## Slide 11
Project team:
Funded by:
more information at www.damsat.org